## Slide 1
Electronic Signals System For Railways Safety
دكتور / حـســيـــن ابـراهـيـم
مهندس / مصطفى الحاجري
- تحت اشراف /
الــفــرقة الــثــانــيــة
برنامج الميكاترونيكس

## Slide 2
OUR CONTENTS
00
WE WILL TALK ABOUT EGYPTION RAILWAYS AND INTRLOCKING SIGNALS SYSTEMS AND DISCUSS SOME ACCIDENTS AND IT,S SOLUTIONS
INTRODUCTION
01
HERE WE WILL EXPLAIN THE SLIPWAY IN PROJECT BY USING ARDUINO UNO AS A CONTROL UNIT, SERVO MOTOR, IR SENSOR, BUZZER
02
IN OUR PROJECT WE USE RF AS A WAY TO PROTECT AGAINST THE COLLISION OF TWO TRAINS IF THEY ARE ON THE SAME DIRECTION OR RAIL
03
IN THIS PART WE WILL EXPLAIN THE FEATURE OF THE LOAD CELL IN OUR PROJECT , AND HOW WE USE IT TO PROTECT PROTECT TRAINS - SLIPWAY
CHAPTER 1 / SLIPWAY
CHAPTER 2/RF WIRELESS TO AVOID TRAIN ACCIDENTS
CHAPTER 3/LOAD CELL PROTECT TRAINS - SLIPWAY
05
HERE WE WILL EXPLAIN THE SLIPWAY IN PROJECT BY USING ARDUINO UNO AS A CONTROL UNIT, SERVO MOTOR, IR SENSOR, BUZZER
CHAPTER 4 / THE SEPARATION OF RAIL CARS
06
RECOMMENDATIONS AND CONCLUSION

## Slide 3
INTRODUCTION

## Slide 4
Progress Company
الهيئة القومية لسكك حديد مصر (س ح م ) تم تاسيسها في عام 1853 و أشرف علي بنائها الخدويوي اسماعيل وهي شركة قطاع عام تمتلكها الحكومة المصرية بالكامل و تشغّل خطوط السكك الحديد المصرية والتي هي الثانية في العالم حيث تأسست بعد تأسيس السكك الحديد البريطانية بفترة وجيزة تعاني اليوم من خلل في منظومة الصيانة و تداعيات إهمال أصابها على مدى عقود فاتت مما يجعل معدل الحوادث عليها أعلى بكثير من نسب باقي دول العالم
و يبلغ عدد المحطات والمواقف و نقط البلوك على الشبكة أكثر من 705 محطة منها عشرون محطة رئيسية في عواصم المحافظات في الدلتا والقناة و الوجه القبلي وبذلك تربط شبكة السكك الحديدية الوادي من أقصاة إلى أدناة على طول أكثر من 1000 كيلو متر و تصل الخطوط الحديدية بين معظم المراكز العمرانية و الاقتصادية في البلاد مثل الموانئ على البحرين الأحمر و المتوسط و مراكز الشحن الخام و المصانع فضلا عن جميع المدن و المراكز الأخرى في شبكة هائلة و متسعة من الطرق الحديدية الحديثة المجهزة لتشغيل جميع أنواع القطارات ذات السرعات العالية عليها. لتأمين السلامة ولمنع الحوادث نحتاج إلى أنظمة تحكم بمسار القطار

## Slide 5
بعض حوادث سكك حديد مصر
2021
18 APR
2021
26 MAR
2021
3 FEB
أثناء مرور قطار 2010 «القاهرة / أسوان» على مزلقان فزارة المطور؛ بين محطتي ديروط والقوصية اقتحمت عربة نصف نقل مجهزة بونش، الحارة المخالفة للمزلقان وهو مغلق مما أدى إلى اختراق غراب الونش الموجود على العربة كابينة جرار القطار؛ ووفاة مساعد سائق القطار و2 من عمال هندسة سكة متواجدين بالجرار.
اصطدام قطار مكيف بقطار ركاب من الخلف بدائرة مركز طهطا بسوهاج ما نتج عنه خروج 3 عربات عن القضبان راح ضحية الحادث 32 مواطنًا وأصيب 108 مواطن.
خرج قطار متجه من القاهرة الي المنصورة عن القضبان قرب محطة سكة حديد طوخ وراح ضحية الحادث عدد من المواطنين بالإضافة إلى إصابة ما يقرب من 103 أشخاص .

## Slide 6
صور بعض الحوادث

## Slide 7
Electronic
Mechanical
Relay system
RAILWAYS
INTERLOCKING

## Slide 8
نظام التحكم الميكانيكي /
نظام التحكم الميكانيكي في السكك الحديدية هو نظام للتحكم عن بعد في التحويلات والإشارات المعدنية وكل العناصر المتحركة الأخرى التحريك عن بعد يتم بنقل القوة العضلية إلى العناصر المعنية عن طريق استخدام الأذرعة الحديدية المرتبطة ببكرات ومسننات وكابلات معدنية
نظام التحكم الكهربائي /
من مميزاته القدرة على تحويل قوانين سير القطارات إلى دارات كهربائية باستخدام الريلاي كما أن من الميزات الشاشة المعدنية رسم عليها مخطط للسكك في المحطة وزودت بمصابيح صغيرة مختلفة الألوان تساعد على تتبع حركة القطارات ومراقبة الإشارات الضوئية.

## Slide 9
نظام التحكم الالكتروني /
في منتصف الثمانينات دخل الحاسوب عالم القطارات وظهر مايسمى بالنظام الإلكتروني للتحكم في السكك الحديدية. يتكون هذا النظام من ثلاث طوابق
طابق المراقبة -- طابق التحكم المركزي -- طابق التحكم
بالعناصر الخارجية
من مزايا النظام الإلكتروني للتحكم في السكك الحديدية
صغر الحجم وأناقة التصميم
سهولة تطوير وتعديل النظام
القدرة الفائقة على تزويد المراقب بالمعلومات الإضافية
ATC

## Slide 10
و بعد كل هذه الحوادث فكرنا في تطوير شبكه السكه الحديد وعمل بعض وسائل الأمان .
Rf WIRELESS
Load cell sensor
Servo motor - IR
LED

## Slide 11
CIRCUIT IDEA
When The Train Passes In Front Of The First Sensor, The Servo Motor Rotates 90 Degrees And An Alarm Bell Alerts Pedestrians At The Crossing. When The Train Passes Completely And The Second Sensor Receives A Physical Signal From The Movement Of The Train, The Engine Will Return To Its Normal Position And The Alarm Bell Will Stop Working.
IR SENSOR - SERVO MOTOR CIRCUIT

## Slide 12
CIRCUIT COMPONENTS
1st
2st
3st
4st
2 Sensor IR
Servo Motor
Alarm
control unit Arduino uno

## Slide 13
CONFIGURATION
WORKING THEORY
Uses
It Is Used In Motion Detectors Used In Construction Services To Operate Lights And Alarm Systems
It Can Detect Colors It Can Be Used Digitally Or Analogue

## Slide 14
SERVO MOTOR
The servo motor is made up of four parts: a normal DC motor, a gear reducer, a position sensor, and a control circuit
A wire (black/brown) is connected to ground, a wire (white/yellow) is connected to the console, and a red wire is connected to the power supply.
2- The engine accepts repeated disconnection and connection operations, no matter how many.
3- High power for the size and power of the engine.
A servo is a motor that allows precise control of angle, acceleration
and speed, capabilities that an ordinary motor does not have
Features of the servo motor:
1- Superfast response, meaning that the engine speed reaches the required value in a short time.

## Slide 15
PROGRAMMING CODE

## Slide 16
CONNECTION OF
THE CIRCUIT
Connecting the sensor :
The two terminals, GRD, 5V are connected to the output of the GRD, 5V on the arduino. The control end is connected to an output from the digital outputs on the arduino.
Connecting the servo motor :
The terminals GRD, 5V, are connected to the output of the GRD, 5V on the arduino and The control terminal is output from the digital outputs in the arduino.
Connecting the alarm bell:
The positive terminal is connected to the output of the Arduino control outputs, and the negative terminal to GND.

## Slide 17
RF TRANSMITTER – RECEIVER
WITH ARDUINO NANO

## Slide 18
RF Transmitter – Receiver
How it works ?
It Works By Detecting A Change In Electromagnetic Properties
It Uses An Electromagnetic Field Rather Than A Purely Magnetic Or Electric Field
Because It Has Magnetic And Electrical Properties At The Same Time.
Why do we use it ?
If We Want To Communicate Some Devices Without Any Wire We RF Modules Is One Of The Ways.
It Is A Device Works To Transmitter And Receiver To Signals
Advantages of RF :
It has a high signal-to-noise ratio which can be maximized by optimizing the sensor design for a particular application.
Unlike inductive sensors its output is speed-independent

## Slide 19
Smart home
Material recycling
Our project /
Connected to two trains if they are within 500 meters of each other and on the same rails the train will be stopped
CONNECTION WITH ARDUINO
Applications

## Slide 20
TRANSMITTER
RECEIVER

## Slide 21
PROGRAMMING CODE RECEIVER

## Slide 22
PROGRAMMING CODE TRANSMITTER

## Slide 23
LOAD CELL PROTECT
TRAINS & SLIPWAY

## Slide 24
On-board weighing
Platform weighing
Belt scales
Hopper scales
Weighing agricultural produce
It converts a force such as tension, compression, pressure, or torque into an electrical signal that can be measured and standardized. As the force applied to the load cell increases, the electrical signal changes proportionally.
Output signal is very small for strain gauge load cells, output signal must go through load cell amplifier to improve signal quality before use by displays or control systems
DEFINITION
APPLICATIONS
HOW IT WORKS?
AMPLIFIER
A load cell is a force transducer. It converts a force such as tension, compression, pressure, or torque into an electrical signal that can be measured and standardized
Load cell sensor

## Slide 25
Connection with Arduino

## Slide 26
PROGRAMMING CODE

## Slide 27
NOTIFY THE DRIVER OF THE SEPARATION OF RAIL CARS

## Slide 28
Knowing the communication between the cars and if a car was separated from the train.
We can control whether the cars on the train are on or off
By placing a LED in each car, and when the car is separated, the LED is Turned off .
CONNECTION FOR THE LED
We control the LED by connecting it to a battery with the train car
COMPONENTS FOR 3 CARS
6 LED -- 1 battery -- Display for 6 LED
CIRCUIT IDEA
Connecting LED positive to battery positive and LED negative to battery negative from the car .
Each LED of a car and with the battery.
Then we connect LED from car to LED that the driver can see it in the driving car, Each LED from the cars is connected to the LED in the display in the driving car via positive with positive and negative with negative .
CONNECTION